## Slide 1: AI-Driven Environmental Monitoring and Shelf-Life Prediction System
Final Semester Project Defense
Food Spoilage Detector
[Add Team Members / IDs]

## Slide 2: Mid-Sem Recap & Final Objectives
The Problem: Post-harvest loss due to poor storage conditions.
Our Objective: Move beyond simple sensor readings to predictive AI.
What We Built (End-Sem Focus):
  • Physics-grounded synthetic data generator.
  • Dual-model Machine Learning Engine (Random Forest + LSTM).
  • Two-stage environmental rules engine.
  • Premium SaaS-style monitoring dashboard.

## Slide 3: Overall System Architecture
Data Ingestion:
  • IoT Sensors capture Temp, RH, CO2, Methane, and Ethylene.
Backend:
  • High-performance Python FastAPI server handling data streams and CSV batch uploads.
Intelligence:
  • Scikit-Learn (Random Forest) and TensorFlow (LSTM) engines predicting Remaining Shelf Life (RSL).
User Interface:
  • React + Tailwind dashboard for real-time visualization.

## Slide 4: Data Generation — The Physics Simulator
The Challenge:
  • Collecting 100,000+ real-world sensor rows is impossible in one semester.
The Solution:
  • We built a strict, physics-grounded simulator to generate training data.
Core Mathematics:
  • Arrhenius Factor: Models exponential biological aging based on temperature.
  • Climacteric Multiplier: Models the sudden spike in respiration and Ethylene during ripening.
Result:
  • Generated over 105,000 rows of highly realistic, scientifically accurate training data.

## Slide 5: Machine Learning Architecture
We evaluated two distinct models to predict Remaining Shelf Life (RSL):
Model 1: Random Forest (Baseline)
  • Treats every sensor reading independently.
  • Fast and highly interpretable.
Model 2: LSTM (Long Short-Term Memory Network)
  • A deep learning model trained on a 48-step sliding window.
Why LSTM?
  • Food spoilage is a time-series problem. How the gas accumulated over the last 24 hours is just as important as the current reading.

## Slide 6: Model Performance & Results
Random Forest Performance:
  • RMSE = 0.077 days.
LSTM Performance:
  • RMSE = 0.043 days (R-squared = 0.9997).
Key Finding:
  • The LSTM almost halved the error rate.
Conclusion:
  • By utilizing the time-history representation (memory of past sensor readings), the LSTM suppresses large errors and provides a highly stable, production-ready prediction.

## Slide 7: Environmental Alert Engine (Traffic Light Logic)
Two-Stage Decision Logic:
  • The system actively monitors the environment for early warnings, not just total spoilage.
Stage 1: Sensor Thresholds:
  • Critical: Methane > 0.5 ppm (Anaerobic rot started).
  • Warning: Temp > 30°C or CO2 > 50,000 ppm (Dangerously hot/suffocating).
Stage 2: Aggregation:
  • Factors are combined with the ML prediction to assign a final actionable status (Green/Raw, Yellow/Ripe, Red/Rotten).

## Slide 8: The Operational Dashboard
We designed a premium, startup-level user interface.
Tech Stack:
  • React, TypeScript, Tailwind CSS (Glassmorphism design), Recharts, and Framer Motion.
Features:
  • Real-time glowing sensor cards (Temp, RH, Gases).
  • Dynamic Area Charts mapping the distribution trends.
  • A giant countdown timer for Remaining Shelf Life (RSL).
[Insert Screenshot of Live Dashboard Here]

## Slide 9: Batch Processing & Analytics
Enterprise Capability:
  • Built a batch-processing engine for warehouse managers.
Functionality:
  • Users can drag-and-drop massive CSV files of raw sensor data.
Analysis:
  • The LSTM engine processes thousands of rows concurrently.
  • Provides a breakdown of dataset status percentages (Raw vs Rotten).
  • Per-row inspections identifying exact confidence and reasons for spoilage.
[Insert Screenshot of CSV Upload Panel Here]

## Slide 10: Conclusion & Future Scope
What We Achieved:
  • Successfully mapped raw chemical gas readings to a highly accurate biological timeline using Deep Learning.
Future Scope:
  • Integrate physical ESP32/Raspberry Pi hardware directly into the WebSocket stream.
  • Train the models on different climacteric fruits (e.g., Avocados, Mangoes).
Questions?
  • Thank you!